# Ice Control with Brine on Highways

# Implementation of Brine Spreading Technologies 
in County of Funen, Denmark

# Lars Bolet

Associate Professor, M.Eng.Sc., Ph.D.*

Aalborg University, Department of Development and Planning

Aalborg, Denmark

bolet@plan.aau.dk

# Summary

During the years 1996-2006, the Division of Highways and Transportation in the former county of Funen gradually replaced pre-wetted salt with brine as de-icing agent in all her ice control activities. The replacement related to 1000 kilometres of highways. Jeopardizing neither road safety nor traffic flow the spread rate of pure sodium chloride (and thus the environmental impact) in the pre-salting operations was cut back by more than one third. Compared to neighbouring counties the use of salt is less than fifty percent per square meter. In addition, supply of brine from two mixer-plants meant that six salt barns could be phased out. This made it possible to revise the staff’s duty roster and thus meet the rest hour demands raised by the health and safety at work acts.

Successful pre-salting is, of course, dependent on reliable weather forecasts and on staff well trained in the art of interpreting this information. The improvements gained by the county of Funen were mainly due to the use of technologies (brine spreading with nozzles) giving a more precise spread pattern than the traditional gritting of pre-wetted salt.

Major challenges in the process have been to verify the higher quality of the nozzles spread pattern, to ensure maximum utilization of volume of brine carried by the spreading vehicles and to control the mixing of brine without getting stratification in the mixture. Moreover, of course, to ensure political approval of abandoning a well-served technology and to organize the replacement of pre-wetted salt so the process was adjusted to the ordinary plan for reinvestments in new spreading material.

# 1. Introduction

It will be possible to reduce the amount of salt spread for pre-salting (and thus reduce the impact on the environment), if salt can be spread more accurately on the target surface of the road, or if one can make the salt stay longer on the road surface. To get the reductions A) technologies have to be developed that can meet the needs, and B) these technologies have to be implemented.

# 2. Spreading technologies

## 2.1 Studies 1998-99 – Brine versus pre-wetted salt on highways

Studies carried out in the winter season 1998-99 by Fyns Amts Vejvæsen (FAV) – i.e. the Highway and Transportation Division in the former County of Funen, Denmark – and the Danish Road Directorate, proved brine to be an interesting ice-control agent compared to pre-wetted salt. During the winter, FAV treated two road stretches with a 20 % solution of sodium chloride (NaCl). Width of the road sections were 5.6-6.0 metre. Nozzles spread the brine, and the spread rate was 20 millilitres brine (4.6 grams pure NaCl) per square meter. FAV used a salt stick, SOBO 20, to measure residual salt 2, 5 and 10 hours after spreading. The measurements took place in six points placed 0.5, 1.5 and 2.5 metres on each side of the road’s centre line. FAV made similar measurements on two road stretches treated with pre-wetted salt but otherwise comparable. The pre-wetted salt was mixed of 70 % (weight) pure; dry NaCl and 30 % brine (20 % solution). Spread rates were 10 or 15 grams pre-wetted salt per square metre (analogous to 7.6 respectively 11.4 grams pure NaCl). Measurements were carried out in 1,800 spots. The conclusions of the study were (1):

- SOBO 20 resistance measurements gives adequate information of the residual salt,

- When using brine, a significantly higher percentage of the salt spread is still present on the road surface 2-10 hours after spreading compared to the use of pre-wetted salt,

- 85-90 % of the brine and 60-65 % of the pre-wetted salt is remaining on the road surface 2 hours after spreading,

- On highways with AADT at 2,500-3,000 vehicles per lane, the residual salt decreases with the number of passing vehicles. A similar correlation was not found on highways with AADT at 500-1,000 vehicles per lane.

FAVs conclusion from the study was that it would be possible to reduce the consumption of salt considerably by using brine-spreading technologies – however the technologies available were still to be improved. By spreading 10 grams pre-wetted salt (7.6 grams pure NaCl) per square metre, one can expect to have 4.9 grams NaCl per square metre (64 %) on the road surface after 2 hours, while the remaining 2.7 grams are dispersed. By spreading 24 grams brine in a 20 % solution (5.5 grams pure NaCl) per square metre, one can expect to obtain 4.9 grams NaCl per square metre (88 %), while only 0.6 grams are dispersed. In other words, compared to the use of pre-wetted salt the environmental impact is reduced by 78 % (2.1 grams pr. square metre) of the NaCl dispersed within 2 hours (without affecting the ice control), or by 28 % of the total amount of NaCl spread. Of course, the result is only valid if one has chosen the spread rate correctly, and if the remaining 4.9 grams NaCl per square metre are uniformly spread on the road surface.

The study failed to prove whether brine would be feasible in all situations with snowfall. FAV continued the study in the winter seasons 1999-2001, but did not obtain any measurements in such snowfall-situations that were considered especially critical.

## 2.2 Studies 2000-02 – Brine versus pre-wetted salt on motorways

Consecutively FAV and the Danish Road Directorate carried out studies to compare the use of brine versus pre-wetted salt on the motorway crossing Funen (E20). The northern lanes, leading from East to West, were treated with pre-wetted salt, while the southern lanes, leading from West to East, were treated with brine.

The study showed (2) that in hoar frost situations, the use of brine instead of pre-wetted salt enables salt savings of at least 30 %. In snow-situations, spreading of brine did not have the same positive effect as spreading of pre-wetted salt on the motorway. In a number of situations, one could observe that both lanes treated with pre-wetted salt turned black, while only the right-hand lane treated with brine became passable. However, the gritter used in the study to spread pre-wetted salt proved to distribute in an imbalanced pattern: More material to the left-hand side (i.e. to the fast lane closest to the centre strip) than to the right-hand side (i.e. the slow lane closest to the emergency lane). Combined with the impact of the traffic (heavy vehicles mainly in the right-hand lane) the imbalance could explain the observations.

Because of this result, it was decided to imbalance the dosage so the right-hand lane of the motorway got 40 % less NaCl (brine or pre-wetted salt) than the left-hand lane. However, while this seemed to be a solution on the motorways, FAV could not implement it on her ordinary highways with traffic in both directions. Instead, it became of vital importance to find gritters that could ensure uniform distribution of the salt.

## 2.3 Measurements 2004 – Spreading patterns

In 2004, FAV carried out measurements of the spreading pattern of all her models of gritters. Individual test-schedules were planned for each model, each schedule consisting of 10 typical situations with variations in spreading width, velocity and dosage. In each situation, the residual salt was measured (SOBO 20) in five cross-sections with a distance of 2 metre, and in each cross-section measurements were taken every 0.5 meter. In total, approximately 7,500 measurements were made. Average and standard deviations were calculated, and the results were compared to the required distributions in the test-schedule, cf. figure 1 showing results from three gritters in comparable situations.

FAV reported the measurements in eight reports (3). The overall conclusion was that the road authorities should explicitly express demands on the quality of the salt-distribution when asking for tenders for gritters. The measuring-programme had provided FAV with experience and procedures to carry out control of whether or not such demands were fulfilled.

Furthermore, the measured spreading patterns from, especially the most modern, nozzle-spreaders showed a better fit to the required uniform distribution than the pattern from spreading pre-wetted salt. FAV found that the measurements imply brine spreading with nozzles to be a promising technology with potential of further improvements towards providing the correct spreading pattern even at high velocities. Contrary to this, spreading of brine and of pre-wetted salt using rotating plates provides dubious spreading patterns and is not likely to offer improvements in the technology.

FAV had not planned the measurements in order to provide data for direct comparisons of the gritters. This makes it somehow hard to establish objective parameters to express the spreading quality. Looking into the measurements of each of the 10 situations in the test-schedules for the gritters, one can however calculate A) the percentage of salt spread (and measured) outside the target-area of the surface, and B) the percentage of salt overdosed in the best-supplied lane, providing that the less supplied lane has received exactly the amount required. Both of these numbers represents waste of salt. For the 10 situations of each gritter, average and standard deviation can be calculated. Staff from the companies that had provided the gritters adjusted the spreaders before the measurements took place. Nevertheless, the average thus calculated may be explained by inaccurate adjustments. The standard deviation, on the other hand, can be interpreted as an expression of the individual gritter’s ability to adjust to various settings of spreading width, velocity and dosage. Figure 2 shows that when using gritters with two technologies (so-called combi-gritters) one should expect far the largest deviations in the spreading pattern, i.e. less precision in the spreading even if the gritter is adjusted as good as could be. This observation confirms that one, if possible, is best off when settling with single-technology spreaders. Gritters using nozzles seem to give slightly smaller deviations than those using rotating plates.

# 3. Implementation

## 3.1 Spreaders

FAV purchased her new brine-spreaders in 2002 and in 2005 – then later completed the investments of equipment to accomplish the implementation of brine for ice control. Both purchases were coordinated with new contracts with contractors to operate the winter maintenance activities, i.e. with redesigning the ice control- and snow-ploughing-routes.

The spreaders purchased used a type of nozzles with an adjustable hole allowing the spreading to take place at a determined constant pressure whatever volume spread. The calibration of these nozzles could be verified simply by collecting brine from each jet in a bucket and weighing it. The type of nozzles also proved the most promising at the measurements conducted by FAV in 2004.

However, when asking for tenders in 2005 FAV put down additional acquisitions and evaluated the biddings by combining the price with effective volume of brine in the spreader’s tank, precision of the spreading, how simple the spreader was to operate and the spreader’s capability to retrieve data giving documentation of location, spreading width and dosage. These requirements led to significant improvements of the effective volume: With the 2002-models, one could benefit approximately 9-m3 brine in an 11-m3 tank, while only 20-litres of the new 14-m3 tank remained after spreading. Furthermore, the collecting of data has proved it possible to determine the dosage of a spreading route with an accuracy of 3 percent, i.e. when planning the activities, one can establish longer routes and still be certain that the spreaders will contain a sufficient amount of ice agent to complete the route.

Additionally, in 2005, FAV installed GPS-technology to control the spreading, i.e. the spreaders would determine the present position by means of the global positioning system and adjust the spreading pattern to variations in lane-width, presence of bus stops, transverse gradient etc. The driver could concentrate on driving the spreading vehicle.

## 3.2 Brine

FAV used to have storages of salt in barns at eight surveillance centres on Funen and at one site on the island of Aeroe. When introducing brine for ice control, FAV had to decide on installing mixing plants at each centre or only a number of the centres. Brine is produced simply by mixing fresh water with pure salt and make sure that all the salt is dissolved. The challenges are A) to get the required quantum, which calls for adequate supply of water and storage capacity and B) to avoid stratification, which calls for equipment to monitor the brine and to ensure continuous circulation.

FAV decided on two plants on Funen. The main argument was the economies of scale: The demand of staff to supervise the plants could be cut back. This was attractive from not only a fiscal point of view but also considering a high average age of the employees and the recognized difficulties of recruiting and due to the legislations of rest hours raised from the health and safety at work acts. Furthermore, the larger plants would ensure supply of brine with the quality prescribed. The plants were established in 1999 and in 2002, and both were enlarged in 2005. The plants were located at two of FAV’s surveillance centres in order to make use of the staff facilities established at the surveillance centres, and to allow the staff to take part in other site-activities when not supervising the mixing plants.

The island of Aeroe is short of subsoil water, and in order not to strain the groundwater resource FAV gained at special permission from the environmental authorities to use seawater for mixing the brine for the island and thus established a small mixing plant at the harbour.

## 3.3 Organisation

The implementation of brine spreading lead to redesigning the ice-control-routes: All the routes on Funen and Langeland had to be readdressed to the two mixing plants, and of course had to be optimized under this condition.

The introduction of GPS-technology meant, of course, that all routes had to be programmed with information of width etc. However, it turned out to be vital as well to instruct thoroughly all the drivers that they had to start on the route where planned and to drive through the route in the planned direction – otherwise the GPS-controlled spreading would be of no use.

Reallocating the staff to the two mixing plants meant that the duty rosters had to involve fewer persons. In a situation where several employees were planning on retiring, this was accepted, at it even made it possible to adjust the rosters so the impact on the staff no longer exceeded the limits laid down by the health and safety at work act, even during severe winter conditions.

The new technologies placed a broader spectrum of challenges upon the mechanics at FAV’s garage. During the period where brine as well as pre-wetted salt was used for ice-control, the number of various types of gritters was high, and each type was unique and required unique skills. Especially combi-gritters, being able to spread brine as well as pre-wetted salt, were skill demanding due to the two different spreading technologies of the gritters. Each mechanic had to specialise, and thus the garage became vulnerable to illness or retirements, and the new advanced technology requires more training to ensure that the garage in all circumstances is fit to fix damages or break-downs.

## 3.4 Political and financial aspects

As all other activities on the road network, the winter maintenance is very visible to the public, and hence changing of technologies are to be considered with respect to the public opinion and the political employers of the highway authority. FAV aimed to inform thoroughly the political committee as well as the press when and why alterations took place, and when new equipment was introduced. The observation is that both parties grew seriously interested in the activity, they were concerned about the environmental impact, but they never questioned the technical decisions made by FAV.

On the island of Aeroe, FAV converted to brine in the winter season 1998/99 – reductions in the consumption of salt and the use of brine based on seawater matched perfectly the islands own branding of giving preference to sustainability, and the change of technology was accepted without any discontent on the island.

On Funen, it was considered also to locate the mixing plants near to the coastline in order to take advantage of the accessibility to seawater. However, the amount of water required to serve the entire county highway network with brine equalised the annual consumption of approximately 1,000 families, and the political committee found this acceptable when considering the logistic benefits of inland locations of the mixing plants.

Purchasing the new brine-gritters in 2002 and in 2005 became a part of FAV’s annual reinvestments of equipment. The price of 40,000 € each was 20 percent cheaper than buying the alternative considered, kombi-gritters being able to spread brine with nozzles as well as pre-wetted salt. FAV had, off course, to adjust other reinvestments, making those replacements a year or two earlier or later than intended, but the overall value of the fleet of equipment was unchanged.

The mixing plants, each at a price of 0.35 million €, were financed by selling two surveillance centres that had become superfluous – the sale even financed improvements of the staff facilities on the remaining surveillance centres.

| Season | Funen | Vejle | Storstrøm | Vestsjælland |
| --- | --- | --- | --- | --- |
| 2005/06 | 1,10 kg/m2 | 2,11 kg/m2 | 2,13 kg/m2 | 2,59 kg/m2 |
| 2006/07 | 0,34 kg/m2 | 0,89 kg/m2 | 0,94 kg/m2 | 0,83 kg/m2 |

Table 1. Consumption of salt (NaCl) per square metre in Funen and in the neighbouring counties, Vejle to the West, Storstrøm to the Southeast and Vestsjælland to the East. The winter 2005/06 was more snowy than normally, while the winter 2006/07 was less snowy. Only the county of Funen used brine spread with nozzles. Reference (4).

# 4. Results

Compared to the neighbouring counties, Funen used less than half the amount of salt per square metre during the winters 2005/06 and 2006/07, cf. table 1.

Table 2 gives the dosages used by FAV on the national highways, where pre-wetted salt as well as brine were still used. The table shows that the dosage of NaCl is 39-65 percent less when using brine compared to the dosage when using pre-wetted salt. FAV used similar dosages of brine on her own highways.

|  |  | Pre-wetted salt | Brine |
| --- | --- | --- | --- |
| Road- and weather- conditions | Temp. | Dosage g/m2 | Dosage g NaCl per m2 | Dosage ml/m2 | Dosage g NaCl per m2 |
| Dry or moisture Risk of hoar frost | > -3 Cº | 10 | 7.7 | 10 | 2.7 |
|  | < -3 Cº | 10 | 7.7 | 15 | 4.3 |
| Moisture or wet Risk of freezing surface | > -3 Cº | 10 | 7.7 | 15 | 4.3 |
|  | < -3 Cº | 15 | 11.6 | 25 | 7.1 |
| Before snow and glass | 15 | 11.6 | 35 | 10.0 |
| For curative treatments | 15 | 11.6 | 35 | 10.0 |

Table 2. Recommended dosages of pre-wetted salt and brine respectively under various circumstances. Used by FAV on the national highways (not motorways) on Funen during winter season 2005/06. The brine used is a 24 % solution. Reference (5).

During the three winter seasons, 2002/03 – 2004/05, where both brine and pre-wetted salt was used on the county highway network of Funen the police reported 48 accidents with slippery roads on the network treated with brine (58 % of the total network) and 40 accidents with slippery roads on the network treated with pre-wetted salt (42 %). The corresponding rates of accidents with slippery roads are 0.08 accidents pr. km pr. year (brine) and 0.09 accidents pr. km. pr. year (pre-wetted salt) respectively. The figures should be interpreted with caution. The parameter ‘road condition’ in the police reports is seldom used for analysis and the quality of the registrations should be examined.

# 5. Main conclusions

Brine can substitute pre-wetted salt for ice control purposes in all situations. Brine is not so likely to blow off the road surface as pre-wetted salt, and the dosage of pure salt (NaCl) can be reduced by one fourth due to this. Brine spread with nozzles is distributed more accurately with a uniform pattern at the target area of the road surface. The dosage of salt can be reduced similarly due to this. These factors mean less impact from salt on the environment.

The rate of accidents with slippery roads does not seem to be higher on roads treated with the lesser amount of NaCl from brine compared to roads treated with ‘normal’ amount pre-wetted salt.

Brine-spreaders’ tank volume can, when designed properly, be utilized at almost 100 % meaning that planned the ice control-routes can be longer. The use of GPS-controlled brine spreading makes it possible to optimize the planning to benefit from almost ‘the last drop’. These factors mean improved day-to-day economy.

Investments in mixing plants have to be made, when introducing brine spreading. The price for various kinds of gritters has only little influence on the overall economy, and the improved day-to-day economy will be able to pay off the investments in mixing plants.

# 6. Final remarks

Until the turn of the year 2006-07 Denmark had three levels of highway authorities. The Danish Road Directorate administered the national highways. The county councils managed the county highways, and the municipalities were in charge of the local road network. Moreover, the municipalities were the authority regarding the private roads.

On Funen, the national highways consisted of 135 km. The length of the county highways was 1.011 km, while the local roads of the 32 municipalities summed up to 5.684 km.

January 1st 2007 the local Danish administration was renewed. A number of municipalities joined into 98 new and larger municipalities. On Funen the old municipalities formed 10 new, including one municipality covering Langeland and another covering the island of Aeroe. Only the “county-capital”, Odense, was unchanged. The reorganisation closed down the Danish counties, and their obligations were distributed among the new local and regional actors. The county highways of major interregional importance became part of the state road network; the remaining highways were included in the municipalities’ local road network. Staff and equipment were divided and transferred with the roads.

FAV’s studies of the use of brine are not prolonged. However, some of the municipalities of Funen are still carrying on their winter maintenance on their major road network along the guidelines and principles laid down by FAV.

# Bibliography

1. Fonnesbech, J.Kr.; (2000). ‘Ice control technology with 20 percent brine on highways’, Transportation Research Board, Issue Number 1741, pp. 54-59.

2. Anonymous; (2003). Prewettet salt versus brine on motorway, Road Directorate, County of Funen, Danish Environmental Protecting Agency and Epoke A/S, Copenhagen.

3. Fyns Amts Vejvæsen; (2004). Saltspredningsmåling. Fyns Amt, Odense, www.plan.aau.dk/~bolet

4. Vejdirektoratet; (2007). Vintertrafik, http://www.vintertrafik.dk/start.asp?file=statistik.

5. Fyns Amts Vejvæsen & Vejdirektoratet; (2005). Vinterhåndbog 2005/2006. Fyns Amt, Odense.

# Footnotes

* Until January 2007 director of the Highway and Transportation Division in the former County of Funen.

# Text boxes

Figure 1. Spreading pattern from three different gritters: A, B and C, all spreading by using a rotating plate. Spreading width is 3 metres on each side of the road centre line, total 6 metres. Gritters A and B are spreading 10 g pre-wetted salt (7.7 g NaCl) pr. m2. Gritter C is spreading 10 ml brine and 3 g salt (5.6 g NaCl) pr. m2. Note that gritters A and B are rotating counter clockwise and overdose to the left, while gritter C rotates clockwise and is imbalanced to the right. Neither of the gritters provide satisfactory spreading pattern. Based on reference (3).

Figure 2. Standard deviations of the percentage of wasted salt from nine series, each of ten sets of measurements of residual salt after spreading with gritters using rotating plates ( (pre-wetted salt or brine), with nozzles ( (brine) or both ▲ (pre-wetted salt or brine). The X-axis shows the standard deviation of the waste of salt due to imbalance between left and right lane of the road, assuming the lane provided with less salt has received just the required amount. The Y-axis shows the standard deviation of wasted salt measured outside the target area of the road surface. Kombi-gritters (▲) using nozzles for brine spreading and a rotating plate for spreading pre-wetted salt tend to have the larger deviation in the percentage of waste. Based on measurements in reference (3).