# CHAPTER 58

INTERACTIVE STRUCTURAL OPTIMIZATION WITH

QUASI-NEWTON ALGORITHMS

C. Pedersen & P. Thoft-Christensen

University of Aalborg, Denmark.

### 1 INTRODUCTION

During the last decades, one of the most important renewals in the fields of structural and especially mechanical design has been the innovation of fully automatic systems and computer based analysis tools. However, fully automated systems are generally not considered feasible or preferable within the field of structural optimization. Therefore, interactive systems and environments are assumed to be used within several engineering fields in the future.

Considering structural constrained optimization problems only, the class of algorithm based on quasi-Newton schemes and algorithms using Lagrange multipliers have proven to be most efficient due to their relatively low number of function and gradient evaluations.

This paper presents a prototype of an interactive optimization system based on a quasi- Newton algorithm, where the designer during the optimization process is able to adjust simple bounds, fix or relax design variables and include/exclude constraints. The optimization is based on a modified quasi-Newton algorithm, which includes a subproblem that minimizes the condition number of the approximate Hessian matrix in each iteration. The purpose is to minimize the condition number of the approximate Hessian matrix and thereby stabilize the determination of the search direction in each iteration after major interactions.

The interactive optimization is carried out through a shell called IROS (Interactive Reliability-Based Optimization System). IROS is mainly intended to constitute a platform for testing of various algorithms and interactive capabilities rather than being a commercial programme. In order to demonstrate some of the facilities of an interactive optimization system, a simple example of a reliability- based optimization of a plane portal frame of steel with I-shaped cross-sections is shown.

# Footnotes

Proceedings IFIP WG 7.5 Conference, Assisi, Italy, September 1994, pp. 225-232.